## Slide 1
Week 2: Classes, __init__ and Inheritance
One interface for every sensor on the vehicle
AI for Aerospace & Mechanical Engineering (PhD)
New content. OOP concepts rewritten from W3Schools (Classes, __init__, Class Properties, Inheritance, Polymorphism) and GeeksforGeeks (class vs instance variables, super(), property(), Abstract Classes, dataclasses, Getting Started with Pytest); ISA model adapted from Anderson, Introduction to Flight, Ch. 3; flat-Earth frame adapted from Groves, Principles of GNSS, Ch. 2.

## Slide 2
Three sensors, one robot
• IMU: 6 numbers at 50 Hz, biased, can saturate
• LiDAR: 16 ranges at 10 Hz, 0.0 or inf when no echo
• GPS: lat, lon, alt, HDOP at 5 Hz, some fixes are garbage
• Every later module (lanes, obstacles, control) consumes them
• Q: how do we add a 4th sensor without editing everything?
Visual: Top view of a small ground robot with three labelled sensors (IMU in the body, LiDAR on the roof with a ring of beams, GPS antenna), each with an arrow to a different raw-data format.
Week 02 | OOP: the sensor hierarchy | 1
Notes: Open with the vehicle, not with Python. Ask the room how they would organise code for three different sensors. Write the final question on the board and keep it there.

## Slide 3
Why the procedural version breaks
• One function per job, an if/elif chain on the sensor type inside each
• Adding a barometer = edit validate, preprocess, to_frame, plot
• Configuration (biases) ends up in globals
• Typos fall through the chain silently
Week 02 | OOP: the sensor hierarchy | 2
Notes: Left grid: the new column touches every function. Right grid: the new sensor only writes the two methods that are really different; the rest is inherited.

## Slide 4
Example 1: the silent typo
• preprocess("imu", raw) removes the bias
• preprocess("IMU", raw) returns raw data: no error
• preprocess("imu", [0.35, -0.05]) accepts 2 values: zip stops early
• Biased data flows into the model unnoticed
Visual: Code block: def preprocess(sensor_type, data): if sensor_type == "imu": ... elif "lidar": ... return data with the three calls and their outputs below; the two wrong outputs highlighted in orange.
Week 02 | OOP: the sensor hierarchy | 3
Notes: Run Section 0 of the lab live. The point: errors that do not raise are the expensive ones.

## Slide 5
Class, object, __init__, self
• Class = blueprint; object = one thing built from it
• __init__ runs at creation and stores attributes on self
• Method = function in the class; Python passes the object as self
• Two objects, one class, different state (two QNH settings)
Visual: Code: class SimpleBarometer: def __init__(self, sensor_id, reference_pressure_pa=101325.0): ... def altitude_m(self, p): ... next to two object boxes "baro0 (101 325 Pa)" and "baro_qnh (100 500 Pa)".
Week 02 | OOP: the sensor hierarchy | 4
Notes: Rewritten from W3Schools "Python Classes" and "__init__() Method". Stress that self is just the first parameter; the name is a convention.

## Slide 6
Class attributes vs instance attributes
• Class body: shared by all objects (good for constants)
• self.x in __init__: one per object (state)
• Mutating a shared list leaks data between sensors
• Assignment on an instance shadows; mutation does not
Week 02 | OOP: the sensor hierarchy | 5
Notes: GeeksforGeeks "Class (static) and instance variables". In-class Problem 1 drills this. Rule: mutable state goes in __init__.

## Slide 7
Example 2: ISA altitude by hand
• h = (T0/L) [1 − (p/p_ref)^(RL/g0)], T0/L = 44 330.8 m, RL/g0 = 0.190263
• p = 95 000 Pa: ratio 0.937577, ln = −0.064457
• power = e^(−0.012264) = 0.987811
• h = 44 330.8 × 0.012189 = 540.3 m
• QNH 100 500 Pa instead: 472.2 m (same class, other object)
Week 02 | OOP: the sensor hierarchy | 6
Notes: Do the arithmetic on the board first, then run SimpleBarometer. Exercise 1.1 is the QNH case.

## Slide 8
Properties: attributes that check themselves
• @property: looks like an attribute, runs a method
• Setter validates: rate_hz = 0 raises ValueError
• No setter = read-only (sensor_id)
• Derived values stay consistent: period_s = 1 / rate_hz
• _name: "internal, do not touch" convention
Visual: Code: @property def rate_hz(self) / @rate_hz.setter def rate_hz(self, value): if not value > 0: raise ValueError; arrow from imu.rate_hz = 0 to a red "ValueError".
Week 02 | OOP: the sensor hierarchy | 7
Notes: GeeksforGeeks "Python property() function". Ask: why not store period_s in __init__? Because it would go stale when the rate changes.

## Slide 9
Inheritance and super()
• class Barometer(Sensor): gets every method of Sensor
• Override: same method name, sensor-specific body
• super().__init__(...) lets the parent set up its part
• isinstance(baro, Sensor) is True
• MRO: the order Python searches for a method
Visual: Two stacked boxes Sensor (sensor_id, rate_hz, readings, add_reading, preprocess) and Barometer (reference_pressure_pa, preprocess override) joined by an inheritance arrow.
Week 02 | OOP: the sensor hierarchy | 8
Notes: W3Schools "Python Inheritance" and GeeksforGeeks "super()". Live: print Barometer.__mro__.

## Slide 10
Example 3: follow super() through three classes
• IMU → InertialSensor → Sensor → object
• Each __init__ prints, then calls super().__init__
• Printed: IMU init, Inertial init, Sensor init
• describe() returns "IMU/inertial imu0 @ 200 Hz"
• Forget one super().__init__: AttributeError much later
Visual: Vertical chain of four boxes (IMU, InertialSensor, Sensor, object); down arrows labelled "super().__init__", up arrows labelled "return value of describe()".
Week 02 | OOP: the sensor hierarchy | 9
Notes: In-class Problem 2. Students predict before running. The late AttributeError is the key lesson.

## Slide 11
Abstract base classes: the interface as a contract
• class BaseSensor(ABC) with @abstractmethod validate, preprocess
• BaseSensor(...) raises TypeError: cannot instantiate
• Subclass missing a method (or with a typo) also raises TypeError
• Error at construction, not mid-flight
Visual: Code: class ForgetfulBarometer(AbstractSensor): def pre_process(...) and the resulting TypeError: Can't instantiate abstract class ... with abstract method preprocess.
Week 02 | OOP: the sensor hierarchy | 10
Notes: GeeksforGeeks "Abstract Classes in Python". Week 3 goes deeper (abstract properties, typing).

## Slide 12
Dataclasses: SensorReading
• @dataclass writes __init__, __repr__, __eq__ from the fields
• frozen=True: a logged measurement cannot change (and is hashable)
• slots=True: no per-object __dict__, less memory
• values is a tuple: arrays break == and hash
Visual: Side by side: 15-line ManualReading class vs 6-line @dataclass(frozen=True, slots=True) class SensorReading: timestamp: float; values: tuple[float, ...]; sensor_id: str; is_valid: bool = True.
Week 02 | OOP: the sensor hierarchy | 11
Notes: GeeksforGeeks "Understanding Python Dataclasses". Show FrozenInstanceError live.

## Slide 13
Example 4: IMU bias and saturation by hand
• ±4 g IMU: full scale 39.23 m/s²; bias a = (0.10, −0.05, 0.20), g = (0.8, −0.3, 0.1)
• (0.35, −0.05, 10.05 | 0.8, −0.3, 2.1) → (0.25, 0, 9.85 | 0, 0, 2.0), n = 1.005
• NaN in a_y → invalid, stored raw
• a_z = 39.50 ≥ 39.23 → saturated, invalid: true value unknown
• (1.30, −0.45, 19.80 | ...) → (1.2, −0.4, 19.6), n = 2.003
Visual: Four-row table: raw sample, valid?, preprocessed values, load factor; invalid rows shaded orange.
Week 02 | OOP: the sensor hierarchy | 12
Notes: Same numbers as Lab Section 7 and tests. The last sample is Week 1's worked example; continuity matters for weak programmers.

## Slide 14
The course sensor hierarchy
• BaseSensor owns buffering, time checks, arrays, DataFrames
• Subclasses own only validate() and preprocess()
• IMUSensor, BarometerSensor: in src/aerospace_ai/sensors.py
• LidarSensor, GPSSensor: Assignment 1
Week 02 | OOP: the sensor hierarchy | 13
Notes: Instructor: read sensors.py before class; it also uses __slots__, __init_subclass__ and a deque buffer, which we discuss in Weeks 3 and 4.

## Slide 15
Template method: add_reading
• Algorithm fixed once in the base class
• Steps 3 and 4 delegated to the subclass
• Invalid samples kept raw with is_valid=False
• to_array() returns valid samples only
Week 02 | OOP: the sensor hierarchy | 14
Notes: Name the pattern now; Week 4 covers Strategy, Observer and Factory.

## Slide 16
Example 5: the Week 1 log through IMUSensor
• Calibrate biases from t < 25 s (parked, level)
• Feed 14 940 samples; ±4 g full scale
• 3 spikes (≈ 50 m/s²) rejected as saturated
• Peak load factor 1.81 g: below the 2.0 g limit
• Week 1 needed a rolling median; here the object knows its limits
Week 02 | OOP: the sensor hierarchy | 15
Notes: Lab Section 9. Caveat: rejection works here because the spikes exceed full scale; spikes inside the range still need filtering.

## Slide 17
Polymorphism: one loop, many sensors
• for sensor in suite: sensor.add_reading(t, raw)
• No if/elif on types anywhere
• A new ThermometerSensor joins with zero changes to the loop
• Same call, type-specific behaviour
Visual: Code loop over [IMUSensor, BarometerSensor, ThermometerSensor] printing id, class, channels, readings, rejected.
Week 02 | OOP: the sensor hierarchy | 16
Notes: W3Schools "Python Polymorphism". Exercise 8.1 builds the thermometer (kelvin in, Celsius out).

## Slide 18
LiDAR: beams, angles and missing echoes
• Beam i at −180° + i × 22.5° (16 beams, 360°)
• No echo: 0.0 or inf; dust: 0.05 m < min range
• Unusable beams become NaN, not zero
• Scan valid if ≥ 50 % of beams usable (fog rejects 4 of 50)
• nearest_obstacle(): np.nanargmin on the latest valid scan
Week 02 | OOP: the sensor hierarchy | 17
Notes: Why NaN and not 0: a zero range would be read as an obstacle touching the robot. Assignment 1, Tasks 4 to 6.

## Slide 19
Example 6: GPS to local metres by hand
• 1° latitude = Rπ/180 = 111 195 m (R = 6 371 km)
• 1° longitude = 111 195 × cos φ0; at Mehrabad (35.69°): 90 314 m
• 0.001° N and E of origin → (east, north) = (90.3, 111.2) m
• Reject: HDOP > 5, NaN, |lat| > 90°
Week 02 | OOP: the sensor hierarchy | 18
Notes: Flat-Earth approximation adapted from Groves, Ch. 2; error below 1 cm over 80 m. Forgetting cos φ0 is one of the grader's mutants.

## Slide 20
Testing classes with pytest
• test_*.py files, test_* functions, plain assert
• pytest.raises: the error must happen
• @pytest.mark.parametrize: one test, many inputs
• @pytest.fixture: a fresh object per test
• Good tests check numbers, not just types
Visual: Code: fixture imu(), test_imu_removes_bias, parametrized test_rate_must_be_positive; terminal line "41 passed".
Week 02 | OOP: the sensor hierarchy | 19
Notes: GeeksforGeeks "Getting Started with Pytest". Assignment 1 grades students' tests by running them against three subtly broken implementations.

## Slide 21
This week's work
• Lab: notebooks/week02/week02_oop_sensors.ipynb (5 TODO exercises)
• In class: 4 warm-ups (shared list, super chain, IMU by hand, climb rate)
• Assignment 1: LiDAR + GPS sensors + your pytest suite, about 4 h, due Week 3
• python -m pytest assignments/assignment01 before you push
Visual: Three icons: notebook, pencil, Git branch.
Week 02 | OOP: the sensor hierarchy | 20
Notes: Assignment 1 hidden tests check numbers from the provided CSVs; the expected-output table in the notebook lets students self-check.

## Slide 22
What We Now Know How To Do
• Bundle data and behaviour in classes; use __init__ and self correctly
• Guard state with properties; keep mutable state per object
• Reuse with inheritance and super(); enforce interfaces with ABCs
• Write records with frozen dataclasses; process sensors polymorphically
• Test a class hierarchy with pytest
Visual: The opener's robot with its three sensors now all pointing into one box "BaseSensor interface", green check marks on each.
Week 02 | OOP: the sensor hierarchy | 21
Notes: Return to the opener question: a fourth sensor is one new subclass with two methods.